Code Refractor
Optimizing Stack-based Vms
Student
Khlud Ciprian
Coordinator
PhD Ferucio Laurențiu Țiplea

---
Code Refractor - Content
Conclusions
1. Performance vs .Net
2. Questions !?
Note: put questions at any moment if things are not clear, is better to interrupt.
1. - Stack-based Vms
2. - Code Refractor architecture
3. - FrontEnd
4. - Optimization overview
5. - Local Optimizations
6. - Use-Def optimizations
7. - DataFlow optimizations
8. - Constant propagation
9. - Escape analysis

---
1. - Stack-based Vms
Java, .Net
All math operations and assignments are using an evaluation stack
They are both stack and register Vms (by means of using local variables)

---
2. - Code Refractor architecture
Read IL→ Interpret → CR IL Code → Optimizations → Optimized CR IL Code → C++ code generation → C++ Code → Compile

---
3. - FrontEnd
Looks for input assembly
Using Mono.Reflection to get IL code
Scan for various Call instructions to fill the call-graph
Interpret instructions into CR equivalent in which instructions are grouped by semantics

---
4. - Optimization overview
Optimizations can be defined by scope:
- one instruction range: various constant evaluations
- block based optimizations
- global (whole function)
- program wide (in C++: Link time optimizations)

---
7. - DataFlow optimizations
DFA Optimizations:
- try to assert some assumptions
- go over whole flow of the code and rafinate assumtions until stabilize the call flow
- it has states before and after instructions

---
8. - Constant propagation
Constant Propagation
X = 2
(…) //X is not modified in this block
A = X //which value is X here?
- using DFA and keeping a constant table before every instruction. If already defined constant is defined (with other constant), this variable is defined invalid

---
9. - Escape analysis
Two analysis:
- Parameter based escaping: required for inter-procedural calls
- Variable based escaping: inside the function
Combined result will (where possible):
- convert smart pointers to raw pointers
- convert heap smart pointers to stack allocations

---
Conclusions 1. Performance vs .Net
Benchmarks show improved performance:
* in math computations
* in memory usage
Slower in:
* when CR optimizations are not applied
* allocation rate

---
2. Questions ?
Questions?

---
Code Refractor
THANK YOU
Optimizing Stack-based Vms
Khlud Ciprian
Coordinator
PhD Ferucio Laurențiu Țiplea